## Slide 1
Stefano Fazzini, MD, PhD
Vascular Surgery
Tor Vergata, University of Rome
Intravascular lithotripsy
As vessel prep for calcified plaques in carotid artery stenting

## Slide 2
Patient description
Patient History
  63 YRS OLD, MALE (BLINDNESS SINCE 40 YRS, Congenital Retinitis Pigmentosa)
  CAD, COPD, PAD (BILA RUTH 3), ACTIVE SMOKING
  BILATERAL ASYMPT CAROTID STENOSIS (RT 80-90%, SN >90%)
  RIGHT CAS ONE MONTH BEFORE (TYPE IV NIC, TERUMO ROADSAVER)
  CALCIFIC >90% ICA STENOSIS, PLANNED FOR CEA >>> CAS
  COMORBIDITIES, ABSOLUTE REFUSAL OF THE PATIENT
  BECAUSE OF HIS BLINDNESS AND THE RISK OF PERIPHERAL NEUROLOGICAL COMPLICATION OF CEA

## Slide 3
Description of the procedure
  Type II calcified aortic arch, moderate vessels tortuosity
  Left ICA, 90% stenosis
  Eccentric 90% (PSV 600 cm/sec) and fully calcific plaque (Type V Nicolaides)
  Vessel Prep by using INTRAVASCULAR LITHOTRIPSY
  Ongoing Dual antiplatelet therapy
  Local anesthesia

## Slide 4
LEFT ICA: Preoperative DUS/CTA

## Slide 5
Strategy and approach
  Image and brief description
  Lt femoral 6Fr access
  90 cm Introducer Sheath (Penumbra Neuronmax)
  Left CCA/ECA cannulation (Sim + Terumo Advantage 0.035)
  Lesion + Cerebral 2D angiograms
  Devices used
  90 cm Introducer Sheath (Penumbra Neuronmax)
  Terumo Advantage 0.035
  Boston Filter Wire EZ
  Sterling 3 x 20 mm (Predilatation)
  Shockwave IVL M5+ 5.5 mm (6 Cycles, 180 pulses)
  IVUS (Philips)
Stent implantation
  Stenting area (ICA / CCA)
    Size of target vessel location: Proximal diameter (mm): 6.6 mm Distal diam. (mm): 5.5 mm. Length: 40 mm
    Specify stent size
    Stent used: TERUMO ROADSAVER Diameter (mm):7 mm Length (mm): 25 mm
  Post dilatation
    Yes Balloon size: Sterling 5 x 20 mm

## Slide 6
Cannulation and preoperative angiograms

## Slide 7
Preoperative angiogram
PRE IVL

## Slide 8
Vessel Prep: IVL (6 cycles), multiple projections

## Slide 9
Completion (post stenting) angiogram
POST
STENT

## Slide 10
Vessel Prep (IVL) and carotid stenting
PRE IVL
POST
IVL
POST
STENT
Shockwave IVL M5+ 5.5 mm + Terumo Roadsaver 7 x 25 mm

## Slide 11
Final angiogram + IVUS

## Slide 12
Filter retrieval (check), Final cerebral angiogram
No Symptoms, Pt discharged after one day

## Slide 13
Follow-up: Post-op and 3 months DUS
Post-op DUS
3 M DUS

## Slide 14
Key Takeaways
  The severe calcium could not be considered a strict contraindication for CAS in every patients
  By using intravascular lithotripsy it’s possible to improve carotid compliance by fracturing calcific (concentric/eccentric) plaque and allowing a safe carotid stenting without improvind embolization rates
  Vessel prep by IVL could be beneficial in some selected case with contraindication for open surgery and calcified carotid plaque
  Peripheral IVL has pros (more powerful/less cycles needed) and cons (60 mm length, OTW platform) compared to coronary IVL
  In the next future, a new platform and sizing could be ideal to use IVL in carotid district